CC.Lake Violet DD3

- PRODUCT:

Name			:  CC.Lake Violet DD3

Chemical Class		:  Triarylmethane toner

Colour Index Name	:  Pigment Violet 3

Colour Index No.		:  42535 :4

CAS No.		:  68647-35-8

EINECS No.		:  271-946-1

Substance Name		: benzénamine, [(amino-4 phényl)(imino-4 cyclohexadiène-2,5 ylidène-1)méthyl]-4, dérivés N-méthyles, molybdosilicates]

- PHYSICAL PROPERTIES:

Density		:   1,85 – 1,90 gr / cm³		Specific Surface		: 37 m² / gr

Moisture Content  : Max. 1%			Water Soluble Content	: Max. 1%

Oil Absorption     :  93 ml / 100 g

pH 		:  7,5 to 8,5

Acid Resistance	: 4				Alkali Resistance		: 2 - 3

- LIGHT FASTNESS  :

Full Tone (1:1)	:  3				Tint Tone (1:10)		   : 2

- WEATHER FASTNESS  :

6 Months	:  1				12 Months		   : 1

- FASTNESS PROPERTIES:

Migration             : 5 (p-PVC)

Ethanol		: 2		Ethyl Acetate	: 4 - 5		MEK	: 1

Butanol		: 2 		Butyl Acetate	: 4		DOP	: 5

Toluene		: 5 		White Spirit 	: 5  		DBP	: 5

Paraffin Wax	: 2		Butter		: 1		Soap	: 2

Water		: 5		Linseed Oil	: 5		Cellosolve: 5

- TECHNICAL COMMENTS:

CC.Lake Violet DD3 is a strong and brilliant blue shade violet pigment only suitable for solvent based flexographic inks and paste inks.

- APPLICATIONS:

Recommended for polyamide and Nitrocellulose Inks. Oil inks.